## Slide 1: “Winlink Express” Pactor setup (formally RMS Express)
Starting with Airmail 2000 for
HF Radio and SCS Pactor TNC setup

## Slide 2
This Power Point will assist you in setting up your HF Radio and SCS Pactor TNC
These are the things you will need to know before you start.
HF RADIO:
Make & Model of your HF Radio
Has the radio got a Serial port or USB to control the radio
What port is it on and the port speed
PACTOR TNC:
Make & Model of you SCS Pactor TNC
Has it got a Serial port or USB to control the TNC
What port is it on and the port speed
Write them down you will need these for use during Airmail & RMS Express setup
HF Radio – Comport ? Speed?
SCS Pactor TNC – Comport ? Speed?

## Slide 3
Newer HF radios have Input and Output level adjustments.
They can be set within the menu system.
Example:
Kenwood TS-480SAT/HX
46 – AF Input
47 – AF Output
Kenwood TS-590
64 – AF Input
65 – AF Output
I find that the Kenwoods are usually best set at 2/2
HF RADIO SETTINGS

## Slide 4
AIRMAIL SETUP
Enter your setting for the TNC & Radio

## Slide 5
Starting AIRMAIL (latest ver. 3.4.062b)
Modules/HF Terminal and make sure the radio and TNC initialize ok

## Slide 6
AIRMAIL (latest ver. 3.4.062b)
Now go to Control/Set PTC-II Amplitude

## Slide 7
AIRMAIL (latest ver. 3.4.062b)
Then in Set PTC-II Amplitude untick the “Track” box then Apply it

## Slide 8
AIRMAIL (latest ver. 3.4.062b)
Note: Radio will transmit when Xmit is clicked
Then in Set PTC-II FSK Amplitude click on Xmit
Adjust - Slider for fast or < > for slow movement while setting transmit for NO ALC
Note: Write down the number in the FSK Amplitude indicated at the top right corner of red box

## Slide 9
AIRMAIL (latest ver. 3.4.062b)
Note: Radio will transmit when Xmit is clicked
Then in Set PTC-II PSK Amplitude click on Xmit
Adjust - Slider for fast or < > for slow movement while setting transmit for NO ALC
Note: Write down the number in the PSK Amplitude indicated at the top right corner of red box

## Slide 10
AIRMAIL (latest ver. 3.4.062b)
At this point you will have the following information.
HF Radio – type of comport, USB or Serial and it ‘s Comport number along with the baud speed
SCS TNC – type of comport, USB or Serial and it ‘s Comport number along with the baud speed
SCS TNC – Level numbers for FSK & PSK

## Slide 11
Winlink Express (latest ver. 1.3.14.0 or newer)
At this point you will enter the setup information that you have written down
In the following screens.
Start - RMS Express and Files/Winlink Express Setup

## Slide 12
Winlink Express (latest ver. 1.3.14.0)
Typical Properties Setup
Add your information. (you will need to be on the internet):
Grid Square go to www.levinecentral.com/ham/grid_square.php
Enter address & Submit and it will show on the map.

## Slide 13
Winlink Express (latest ver. 1.3.14.0)
Open – Pactor P2P Session

## Slide 14
Winlink Express (latest ver. 1.3.14.0)
Pactor P2P Session – TNC start initialization ERROR
You most likely will get an error during initialization
we will fix this in the following slides

## Slide 15
Winlink Express (latest ver. 1.3.14.0)
Pactor P2P Session – TNC parameter Setup
Click on the Setup tab

## Slide 16
Winlink Express (latest ver. 1.3.14.0)
Pactor P2P Session – TNC setup
Change the following to the same as your info.
Note: PSK is first followed by FSK
(In Airmail they were reversed so enter FSK to FSK and PSK to PSK)

## Slide 17
Winlink Express (latest ver. 1.3.14.0)
Pactor P2P Session – HF Radio Control Setup
Your parameters may vary…
Enter your - Port, Speed, Type of HF Radio etc.

## Slide 18
Winlink Express (latest ver. 1.3.14.0)
Pactor P2P Session – TNC initialization OK

## Slide 19
Winlink Express (latest ver. 1.3.14.0)
Pactor P2P Session – TNC to Radio Level Setup
The Airmail numbers get you close to No ALC easier than using RMS Express does
Test using the Winlink Express Level test and do a final adjust for NO ALC
Exit the program to save the parameters